## Slide 1
Proximity Effect in EBL
by:
Zeinab Mohammadi
November 2011
Electrical and Computer Engineering Department
University of Victoria

## Slide 2
Outline
Definition
Origins
Avoidance of Proximity
Correction

## Slide 3
Definition
The proximity effect is the change in feature size of pattern as a consequence of nonuniform exposure!
Pattern affected by proximity (left), After elimination of proximity effect (Right)

## Slide 4
Electron-Solid Interactions
Forward Scattering Backward Scattering
Secondary Electrons
Notes: In order to know what exactly happen, it is worthwhile to look at to electron beam interactions.

## Slide 5
Forward Scattering
As the electrons penetrate the resist, they experience many small angle scattering events, which tend to broaden the initial beam diameter.

## Slide 6
Backward Scattering
As the electrons penetrate through the resist into the substrate, they occasionally undergo large angle scattering events

## Slide 7
Secondary Electrons
As the primary electrons slow down, much of their energy is dissipated in the form of secondary electrons with energies from 2 to 50 eV and this energy accumulates around patterned areas!
High energy!
Low energy!

## Slide 8
Proximity Effect Avoidance
Adjust the pattern size
Exposure of low energy e-beam
Multilayer resists coating techniques

## Slide 9
Correction
Dose Modulation
Background Exposure Correction (GHOST)
Software
Very common technique with good resolution
Time consuming
No computation required
Extra data preparation and writing time, less resolution

## Slide 10
Conclusion
Proximity effect concepts reviewed
Reason why it happens discussed
Techniques to avoid and correct it considered

## Slide 11
Any Questions?!