## Slide 1
Scanning electron microscope (SEM)
ELECTRON SOURCES
Ruth Jaimes
2013
CAMTEC Nanofabrication Workshop
Hitachi S-4800 field emission scanning electron microscope

## Slide 2
CAMTEC Nanofabrication Workshop
What is the main idea of SEM?
Electron gun
How is a fine electron bean formed?
Haw can we obtain an even finer electron bean?
What kinds of electron guns (electron sources) are used in the SEM?
What are the differences between the kinds of electrons guns?
ELECTRON SOURCES

## Slide 3
SEM ELECTRON SOURCES
The electron gun are located either at the very top region of the SEM that generates a beam of electrons
CAMTEC Nanofabrication Workshop
A scanning electron microscope (SEM) is a type of electron microscope that produces images with a focused beam of electrons.
The electrons interact with electrons in the sample
The electron beam is generation by electrons sources.
These electrons don't naturally go where they need to, however, which gets us to the next component of SEMs.
Configuration of SEM
The mechanism that emits electrons
form a metal and accelerates them
a strong electric field.
What is the main idea of SEM?

## Slide 4
CAMTEC Nanofabrication Workshop
How is a fine electron bean formed?
The electron source (diameter do) formed by electron gun is reduced and made into a fine electron bean (diameter dk) by the condenser lens and objective lens.
Haw can we obtain an even
finer electron bean?
In order to obtain a fine electron bean,
the instrument utilizes an electron gun featuring:
a small electron source,
a large current density (current (in A/cm2) per unit area, and
a small energy width (energy vitiating (in eV) of discharged electrons.
SEM ELECTRON SOURCES

## Slide 5
Why is important the electron sources?
The simplest and cheapest gun uses a heated tungsten wire to produce electrons.
generates a beam of electrons
What kind of electron sources is used in the SEM?
Em um MEV típico, os elétrons são emitidos termionicamente a partir de um cátodo (filamento) de tungstênio ou hexaboreto de lantânio (LaB6) e acelerados através de um ânodo, sendo também possível obter elétrons por efeito de emissão de campo. O tungstênio é tipicamente usado por ser o metal com mais alto ponto de fusão e mais baixa pressão de vapor, permitindo que seja aquecido para a emissão de elétrons.
CAMTEC Nanofabrication Workshop
Field emission guns, create a strong electrical field to pull electrons away from the atoms.
Thermionic guns type, apply thermal energy to a filament (usually made of tungsten, which has a high melting point)
- cold field emission,
- Schottky,
- tungsten,
- LaB6 (lanthanum hexaboride)
There are three types of electron gun according to the method of emission:
- field emission type (FE) electron gun,
- Schottky electron gun and,
- thermal electron gun.
Notes: “SEM electron sources – cold field emission, Shottky, tungsten, Lab6”

## Slide 6
CAMTEC Nanofabrication Workshop
What kind of electron sources is used in the SEM?
(a) Thermionic gun (tungsten)

## Slide 7
CAMTEC Nanofabrication Workshop
What kind of electron sources is used in the SEM?
(b) LaB6 gun

## Slide 8
CAMTEC Nanofabrication Workshop
What kind of electron sources is used in the SEM?
(c) cold field emission (FE) electron gun

## Slide 9
CAMTEC Nanofabrication Workshop
What kind of electron sources is used in the SEM?
(d) Schottky electron gun

## Slide 10
CAMTEC Nanofabrication Workshop
What are the differences between the kinds of electrons guns?
SEM ELECTRON SOURCES

## Slide 11
CAMTEC Nanofabrication Workshop

## Slide 12
CAMTEC Nanofabrication Workshop
  Thanks for attention
Canada
Brazil
Victoria BC